## Slide 1
DIGITAL LOGIC DESIGN PROJECT
4-Bit Synchronous
Up/Down Counter
With seven-segment display output
Q3
3
Q2
2
Q1
1
Q0
0
Clocked digital system
Prepared for project presentation

## Slide 2
02
Project objective
A synchronous counter changes all four output bits on the same clock edge
Count upward
0000 to 1111
Select direction
with one control input
Count downward
1111 to 0000
UP/DOWN = 1
UP/DOWN = 0
The display presents the 4-bit output as hexadecimal digits 0–F.
Design and Simulation of a 4-Bit Synchronous Up/Down Counter

## Slide 3
03
System architecture
Three functional blocks form the complete project
CLOCK
source
4-BIT SYNCHRONOUS
UP/DOWN COUNTER
4-BIT TO 7-SEGMENT
DECODER
7-SEGMENT
DISPLAY
UP/DOWN control
RESET
Q3 Q2 Q1 Q0
Design and Simulation of a 4-Bit Synchronous Up/Down Counter

## Slide 4
04
Synchronous counter operation
Every flip-flop receives the same clock signal
Shared clock
CLK
D FLIP-FLOP
Q0
D0
D FLIP-FLOP
Q1
D1
D FLIP-FLOP
Q2
D2
D FLIP-FLOP
Q3
D3
All outputs update together at the active clock edge. This avoids ripple delay between bits.
Design and Simulation of a 4-Bit Synchronous Up/Down Counter

## Slide 5
05
Direction control and state sequence
The UP/DOWN input selects the next binary state
UP/DOWN = 1 | Increment
UP/DOWN = 0 | Decrement
0000
0001
0010
…
1111
0000
1111
1110
1101
…
0000
1111
Wraparound: 1111 returns to 0000 when counting up; 0000 returns to 1111 when counting down.
Design and Simulation of a 4-Bit Synchronous Up/Down Counter

## Slide 6
06
Implementation options
Choose the approach that matches your course requirements
Logic design with flip-flops
• Four D flip-flops
• Combinational next-state logic
• One shared clock
Counter IC or simulator block
• Configure a 4-bit synchronous counter
• Connect UP/DOWN and reset
• Observe outputs on the display
Either approach must demonstrate synchronous counting, direction selection, reset, and wraparound.
Design and Simulation of a 4-Bit Synchronous Up/Down Counter

## Slide 7
07
Seven-segment display interface
The decoder converts four binary inputs into seven segment control signals
Q3 Q2 Q1 Q0
HEX / BCD TO
7-SEGMENT DECODER
a b c d
e f g
Display examples
0000 = 0 1001 = 9 1010 = A 1111 = F
Design and Simulation of a 4-Bit Synchronous Up/Down Counter

## Slide 8
08
Simulation and test plan
Demonstrate each required behavior with screenshots or a live simulation
Test
Function
Action
Expected result
1
Reset
Press reset
0000 and digit 0
2
Up count
Apply clock pulses with UP/DOWN = 1
0, 1, 2, …, F, 0
3
Down count
Apply clock pulses with UP/DOWN = 0
F, E, D, …, 0, F
4
Clock check
Inspect all Q outputs at one edge
All bits change together
Design and Simulation of a 4-Bit Synchronous Up/Down Counter

## Slide 9
Conclusion
The project combines sequential logic with a visible output device.
1
Synchronous operation
One common clock updates all bits together
2
Direction selection
The control input chooses increment or decrement
3
Visible verification
The display shows each 4-bit state as 0–F
Thank you